## Slide 1: Principal Engineer’s Update
Randall Wayth - July 2023 project meeting

## Slide 2: Outline
    Early MWA engineering
    MWA Development
    The Phase II era
    The MWAX era Part 1: signal (un)chained
    The MWAX era Part 2: towards real-time beamforming
    The future

## Slide 3: Early MWA Engineering
  MIT Haystack: (PE: Roger Cappallo, Guru: Alan Rogers + team)
  Antenna/LNA, beamformer - Eric Kratzenberg & Brian Corey
  Clock
  FinePFB/correlator – CSIRO + Haystack
  RRI: (Prabu T, Vani, G-K + team)
  Digital systems (ADFB, AgFo)
  ANU (Guru: Frank Briggs, Mark Waterson + team)
  Analogue Signal Conditioner + Rx
  Melbourne, Curtin: Technical, logistical support
Sep 2005
March 2005. Image: D. Herne

## Slide 4: Development – Original Concept
  Originally the “Low Frequency Demonstrator”: MWA-LFD
    512 tiles, HW correlator, real-time cal & imaging (FTW!)
Aperture plane
u,v plane
From a 2007 slide…

## Slide 5: Phase 1 era: 128T
    Industry partnerships for hardware and infrastructure
    Wandering guru: Bob Goeke
    Large student/staff cohort part of construction
    Hybrid FPGA/GPU correlator, with very limited parameters, but does the job.

## Slide 6: MWA digital signal path
From Tremblay et al, 2015.
Bespoke protocol
Bespoke protocol
10G ethernet
Software correlator (could run on 6 boxes with current GPU, network)
From June 2016 meeting

## Slide 7: The Phase 2 era
128 New Tiles!
56 new long baselines -> x2 diameter!
Redundant arrays – back in fashion!
Same Rx and signal path: 2 configurations with manual reconfig (time, risk)

## Slide 8: The MWAX era
  Paper published – please cite where appropriate!
  Current/recent activities:
    Coarse channel bandshape correction
    Correct vis weights (e.g. missing or flagged data)
    Static delay corrections
    Fringe tracking available
Working towards real-time beamforming – many subtle details

## Slide 9: New MWA signal path
Rx 17
Rx 18

## Slide 10: New Receivers: NI receiver
    RRI-compatible digital PFB created for these units.
    Units do not have ASCs (no gain, no filtering)
    However, the output power levels from MWA RFoF tiles (after the RFoF link) are fortunately at the right level such that gain is not required
      Only a lowpass anti-aliasing filter
    These units output true 8-bit samples, so have more intrinsic dynamic range than RRI units
Jake Jones + MWA ops
Prototype 8-tile receiver using NI FlexRIO units
RFoF = Radio frequency over fibre

## Slide 11: New Receivers: SHAO Receiver
    Full receiver system
    Designed for signal levels from coax and RFoF tiles
    Data output on standard network interfaces
    Compatibility mode replicates PFB of existing receivers
    Future mode can generate oversampled coarse channels
    Raw voltage capture capability
    Extensive lab testing

## Slide 12: Show live status pages
https://ws.mwatelescope.org/tiles/tilemap/
http://telemetry-static.mwa128t.org/liveplots/

## Slide 13: Show live status pages
https://ws.mwatelescope.org/tiles/tilemap/
http://telemetry-static.mwa128t.org/liveplots/
MWA Currently active tiles

## Slide 14: The Future: From 144T towards 256T
  With a full complement of receivers:
    No array reconfigs! – all antennas available all the time
    Consolidation of signal paths, with new power and aggregation points
    With 32 new Rx, move to oversampled PFB
  A 256T MWA is the same magnitude signal processing as SKA1-Low
From a 2016 slide…

## Slide 15: Questions?
Image: Andre Offringa

## Slide 16: New Receivers: NI Rx “first light” (May 2022)
Jake’s first light plot – looking good!

## Slide 17: What’s new and what’s not?
    Farewell old fine (10 kHz) PFBs
    1.28 MHz coarse channels are the basic data unit flowing in system
    Straightforward to capture raw coarse channels, no inverting fine PFB required
    LOTS of new time/freq modes
      See wiki: https://wiki.mwatelescope.org/display/MP/New+Correlator+-+MWAX
    Same oversampled coarse channels with PFB bandpass edges
    Fringe stopping still applied in post-processing (for now)
    Time and/or bandwidth decorrelation still need to be considered (for now)
New
Not New

## Slide 18: Outline
    MWAX update
    Brief history
      Oct 2014: “Phase II” planning
      June 2016: “Phase III” aspirations
      Many desired enhancements
      Funding secured last year for hardware
    Key to unlocking this: un-hardwire the signal chain
      Move to standard network-based signal chain like most other low frequency telescopes
Brian Crosse
Ian Morrison
Greg Sleap
+ MWA ops team

## Slide 19: Receivers update
    For 10 years, the 16 in-field receivers have serviced MWA
    With Phase II, relocation of receivers is required to change from compact <-> extended configs
    Effectively irreplaceable, it is remarkable that they have survived this long
    NI-based units were acquired a few years ago as potential replacements for the digital part, but could not be (easily) integrated with the old correlator
There’s one…

## Slide 20: New Receivers: NI receiver
    Early in 2022, the LBGx RFoF fibres were re-routed and the prototype installed on site
    Supporting hardware for power, data transport (data networking), and clock deployed
    Standard RFoF optical receivers moved from field
    The clock distribution is new and serves as a prototype for future expansion
M&C network
Clock distribution
Power
RFoF optical-> electrical
NI digital units
Clock
Data transport
Freq synth